## Slide 1
European Conference on EDGE AI
Technologies and Applications - EEAI
19-21 October 2026, Malta
The convergence point of generative intelligence and autonomous action. Edge AI creates, reasons, and acts.

## Slide 2
Graham Pellegrini, University of Malta, Malta
M.AI.ESTRO: Virtual Reality Skill Guidance Through Edge AI

## Slide 3: Presentation Outline
Introduction
State-of-the-art
Research Goal
Methodology
Design and Implementation
Experimental Results
Future Research
Conclusion

## Slide 4: Introduction
Skill transfer today relies on a novice watching and imitating an expert, then practising from memory.
M.AI.ESTRO instead captures an expert's manipulation and replays it as a spatially-aligned “ghost hand” overlay directly on the real object, on a standalone Meta Quest 3 headset.
This guidance is itself a demanding edge-AI problem: segmentation, multi-view reconstruction, 6-DoF pose estimation and a predictive world model, all while the headset stays untethered and battery-constrained.
This talk focuses on the architecture that makes that possible: splitting computation between a thin, always-light client and a GPU cluster.

## Slide 5: State-of-the-art
Immersive guidance research shows physical skill transfer benefits from spatial, in-context instruction, but typically assumes continuous or heavy on-device processing.
Conventional edge AI pushes more computation onto the device to cut latency and cloud dependence.
Standalone XR headsets already sit at a hard compute, power and thermal ceiling, and the industry's likely next step, AR glasses, has a far lower one still.
The open problem is not how much a device can fit, but how little it structurally needs to do.

## Slide 6: Research Goal
Deliver spatially-aligned ghost-hand guidance on a standalone headset, with the device's compute floor pushed toward zero by construction, not as an afterthought.
If sensing and final rendering are the only irreducible on-device work, the same architecture should transfer from a Quest headset to a future, far thinner AR-glasses form factor.
Test this by building the system and measuring, not assuming, where device-side compute actually remains.

## Slide 7: Methodology
Three-stage pipeline: capture on the headset, structured processing on a GPU cluster, replay back on the headset as a ghost-hand overlay.
The headset only ever applies a transform or asset the cluster has already computed; no model inference or geometry fitting runs on-device.
This talk covers the architecture, not the model pipeline recipe; perception and world-model components are described at a high level only.

## Slide 8: Design and Implementation: Thin Client / Fat Cloud
Deliberately the inverse of conventional edge AI: keep the headset's compute floor near zero (sensing and rendering only) and push every model-shaped computation to the cluster, delivered pre-prepared.
Motivation: AR glasses have a far lower compute, power and thermal budget than a Quest headset. A near-zero compute floor has to be true by construction; it cannot be retrofitted later.
This is a deliberate architectural decision confirmed in the deployed code: the client applies a transform or loads an asset the cluster already computed, and never fits one itself.

## Slide 9: Design and Implementation: What’s Validated Today
Mesh delivery: served meshes are reduced to 3–5MB single-file glTF (from 18–65MB raw reconstructions), with conditional-GET caching so an unchanged asset is never re-downloaded.
Replay previously fetched one mask image per object per displayed frame; it now fetches one bundle per object at load time, confirmed on a real headset across repeated sessions.
Net effect: the client's steady-state network behaviour during replay matches the “prepared asset, not a live computation” framing, not only in principle but as measured on-device.

## Slide 10: Design and Implementation: Infrastructure
The GPU cluster absorbs all model-shaped computation; the headset stays a thin client for sensing and rendering only; cloud deployment also buys scalability for heavier or more complex requests over time.
Current routing is standard reverse-proxy dispatch from a shared gateway to the application layer to the Maestro service container; already separated at the infrastructure level as independent services.
Public addressing is still finalising: a dedicated domain is pending, with service-level separation already in place ahead of it.

## Slide 11: Experimental Results: Mesh Delivery
Raw multi-view reconstructions run 18–65MB; served, registered meshes are reduced to 3–5MB single-file glTF before ever reaching the client.
Measured cache behaviour: requesting an unchanged asset returns a cached response rather than a re-transfer, verified against real object versions.
Result: the heaviest single asset the client needs is already an order of magnitude smaller than its raw source, with no further client-side processing required to use it.

## Slide 12: Experimental Results: Mask Delivery Fix
Baseline behaviour: one HTTP request per tracked object per displayed frame during replay, at headset frame rate, for the full replay duration.
Change made: one request per object, fetched once at load time instead.
Verified on a real headset across multiple real sessions and minutes of replay: exactly one list call and one bundle call per object, zero further requests across repeated view changes and idle gaps.

## Slide 13: Future Research
Complete the dedicated public endpoint so Maestro's traffic no longer shares infrastructure with unrelated services.
Move status updates from periodic polling toward a push-based mechanism to remove dead latency.
Scale from individually captured demonstrations toward a structured dataset; downstream manipulation-transfer work is a future direction, not a current result.

## Slide 14: Conclusion
M.AI.ESTRO shows that spatial skill guidance and a near-zero compute-floor device are not in tension: the cluster carries the model-shaped work while the headset stays thin, today, on real hardware.
One verified result: replay-time network behaviour now matches the thin-client framing, not just the architecture diagram.
One open limitation: the device still reaches the cluster through shared infrastructure; a dedicated endpoint is the immediate next step toward the architecture this talk describes.

## Slide 15
graham.pellegrini@um.edu.mt
For your attention
Copyright © 2026
Thank You

## Slide 16: Event Organisers
SMARTY - Scalable and Quantum Resilient Heterogeneous Edge Computing enabling Trustworthy, focuses on cloud-edge continuum for heterogeneous systems, that protects data-in-transit and data-in-process, employing novel accelerators for quantum resilient communications, confidential computing, and software defined perimeters. https://www.smarty-project.eu/
EdgeAI (Edge AI Technologies for Optimised Performance Embedded Processing) develops new electronic components and systems, processing architectures, connectivity, software, algorithms, and middleware through the combination of microelectronics, edge AI, embedded systems, and edge computing. www.edge-ai-tech.eu
EdgeAI
NEUROKIT2E
SMARTY
dAIEDGE
dAIEDGE is the European Network of Excellence for distributed, trustworthy, efficient, and scalable AI at the Edge and promotes the application, development, and deployment of Artificial Intelligence (AI) on edge computing platforms. https://daiedge.eu/
NEUROKIT2E (Open source deep learning platform dedicated to Embedded hardware and Europe) proposes a Deep Learning Platform for Embedded Hardware around an established European value chain (AI HW/SW). The solutions developed support neural network design, optimisation, and implementation on constrained HW. https://www.neurokit2e.eu/
NEUROKIT2E

## Slide 17: Event Organisers
REBECCA (Reconfigurable Heterogeneous Highly Parallel Processing Platform for safe and secure AI) aims to democratize the development of edge AI systems and create a complete hardware and software stack centered around a RISC-V CPU, which offer higher performance, energy efficiency, safety, and security than existing systems. www.rebecca-chip.eu
TRISTAN aims to expand, mature, and industrialize the European RISC-V ecosystem to compete with commercial options by leveraging the Open-Source community to gain productivity and quality. A European strategy for RISC-V designs will be defined, creating a repository of industrial rate building blocks for SoC designs in various application domains. www.tristan-project.eu
CLEVER (Collaborative edge-cLoud continuum and Embedded AI for a Visionary industry of thE futuRe) proposes innovations in hardware accelerators, design stack, and middleware software that revolutionize the ability of edge computing platforms to operate federated, leveraging sparse resources that are coordinated to create a powerful swarm of resources. www.cleverproject.eu
SMARTEDGE
TRISTAN
CLEVER
REBECCA
The SmartEdge project aims to achieve dynamic integration of decentralized edge intelligence while prioritizing reliability, security, privacy, and scalability. The SmartEdge solution includes a low-code tool programming environment with three main tools: Continuous Semantic Integration, Dynamic Swarm Network, and Low-code Toolchain for Edge Intelligence. https://www.smart-edge.eu/

## Slide 18: Event Organisers
The objectives of LoLiPoP IoT (Long Life Power Platforms for Internet of Things) are to develop energy harvesting-based innovative Long Life Power Platforms that enable retrofit of wireless sensor network edge devices for asset tracking, condition and performance monitoring. www.lolipop-iot.eu
LoLiPoP IoT
EdgeAI-Trust
AIMS5.0
MOSAIC
The MOSAIC project aims to achieve European technological independence and digital autonomy in Electronic Components and Systems (ECS) for automated systems, aligning with the EU Chips Act. It will develop next-generation, energy-efficient, and robust cognitive ECS, focusing on integrating diverse perception hardware and fostering interoperability to gain a competitive advantage for European manufacturers. https://chips-mosaic.eu/
EdgeAI-Trust addresses an advanced, trustworthy edge AI ecosystem through cutting-edge hardware, software, and tools. The project aims to enhance decentralized EdgeAI operations that are secure, reliable, and sustainable. By integrating AI-based algorithms, devices, and APIs, EdgeAI-Trust fosters interoperability and secure data exchange across diverse platforms. from sensor-actuated devices to cloud systems, all within a dynamic zero trust environment. https://www.edgeai-trust.eu/
AIMS5.0 aims to boost the economy by adopting, extending, and implementing AI-enabled HW and SW components and systems across the entire industrial value chain. New technologies from IoT and based on Semantic Web ontologies, ML and AI help European manufacturers to shift from Industry 4.0 to Industry 5.0, creating human-centric workplace conditions and a climate-friendly production. https://aims50.eu/

## Slide 19: Supporting Organizations
The European Technology Platform on Smart Systems Integration is an industry-driven policy initiative, defining research, development and innovation needs as well as policy requirements related to Smart Systems Integration and integrated Micro- and Nanosystems. The main objective is to develop a vision and to set up a Strategic Research Agenda. www.smart-systems-integration.org
Inside Industry Association is the European Technology Platform for research, design and innovation on Intelligent Digital Systems and their applications. The Association is a membership organisation for the European research and innovation actors with more than 200 members and associates from all over Europe. www.inside-association.eu
Chips Joint Undertaking supports research, development, innovation, and future manufacturing capacities in the European semiconductor ecosystem. Launched as part of the Chips for Europe Initiative, it confronts semiconductor shortages and strengthens Europe's digital autonomy, engaging a significant EU, national/regional and private industry funding of nearly €11 billion. https://portal.chips-ju.europa.eu/
EU
AENEAS
EPoSS
INSIDE
Chips JU
AENEAS standing for Association for European NanoElectronics ActivitieS, is an industrial Association, established in 2006, providing unparalleled networking opportunities, policy influence & supported access to funding to all types RD&I participants in the field of micro and nanoelectronics enabled components and systems. https://aeneas-office.org/